## Slide 1: “The internet and Ham Radio interconnected”
What does Part 97 say ???

## Slide 2: Internet and Ham Radio
Internet assisted Amateur Radio (also called VoIP) has had a major effect on information transfer and Amateur Radio. The name of the protocol depends on the type used. It can be EchoLink, the Internet Repeater Linking Project, and some other means.

## Slide 3: What parts of Part 97 governs VoIP
All of them, or none of them!
It depends on whether your asking about the
“VoIP assisted” or the “Amateur Radio” part of
VoIP-assisted Amateur Radio.

## Slide 4: The FCC does not care about the Internet part! Are there any rules which such an operation should follow?
The main points to remember are:
  All stations must be controlled.
  Only certain types of stations may be automatically controlled.
  Simplex Voice Stations may not be Automatically controlled.
  Any station under remote wireless control must utilize an Auxiliary Station operating on 222.15 Mhz or above.

## Slide 5: Two automaticlly controlled repeaters are linked via VoIP. Is this legal?????
YES!!! Forget the VoIP link. That is the internet. Repeaters are legal. This is the same as ANY other wired link. The system and its software must:
1. Exclude NON hams from accessing the repeaters unless a control operator is present at the control point.
2. Prevent the initiation by a nonham of a message via an Amateur Station without the presence of a Control Operator.

## Slide 6: Are automatically controlled simplex nodes LEGAL???? “N O”!!!!!
Only a few types of stations may be operated unattended, under automatic control.
Space Stations, Repeaters, Beacons, Auxiliary Stations and certain data or RTTY Stations.

## Slide 7: LOCALLY OR REMOTELY CONTROLED What does that mean????
A simplex VoIP node may be locally controlled by an operator who is at the node.
A node may be remotely controlled at some other point with the operator issuing commands via a wireline or radio control link.
If radio it must be an auxiliary station which must operate at 222.15 MHz or above.
Below are a few examples……...

## Slide 8
A control op. is stationed and active at the VoIP node on any frequency. This is a locally controlled station, like a typical operation on FM simplex. IS THIS LEGAL?????
A control op. communicates with and controls a simplex VoIP node with an HT xmitting and listening to the node on 223.52 MHz.
IS THIS LEGAL?????
A control op. performs as above but on 147.41 MHz. IS THIS LEGAL?????

## Slide 9
A control op. operates a simplex VoIP node at 147.41 MHz and is stationed at the node’s transmitter. Users access on the same frequency.
Is this legal????
A control op. operates a simplex VoIP node at 147.41 MHz. The control op. continually monitors the nodes transmissions and can call a dedicated telephone line or use a dedicated internet connection to turn the node on and off. User stations access the node on the same freq.
IS THIS LEGAL

## Slide 10
A control op. communicates with and controls a simplex VoIP node with a multi-band HT, continuously monitoring the node on 147.41 MHz. He or she sends power on/off commands with the same HT on 223.52 MHz.
IS THIS LEGAL?????
Same configuration as either of the above two situations, except the op. does not continuously monitor the nodes transmissions.
IS THIS LEGAL?????

## Slide 11: What This Means
The Part 97 Rules cover the operation of Radio Stations in the Amateur Service.
The basic rules do NOT change just because the internet is involved. It is just like any other wire line.
Except in certain situations, unattended Amateur Station operation is not permitted. When permitted it is called Automatic Control.
It is allowed only for Space Stations, Beacons, Auxiliary Stations ( which must operate at 222.15 MHz or above, and certain RTTY and data stations.

## Slide 12
The information presented was taken from the FCC RULE BOOK, 13th Edition, as published by the ARRL. It has been edited for space. Please refer to this book when trying to understand Part 97, which is included in full.
There are some changes which may be placed in Part 97 concerning the frequencies required by Auxiliary Stations. Until they take place and become official only follow the active rules.
You can request changes to Part 97 and comment on possible changes by following FCC procedures.